| 140actual viewing angle. (With less viewing angle the viewed object is larger compared to the 160 mirrors.) Both indoor or outdoor versions. Adjustable mounting bracket(s). T-304 STAINLESS STEEL mirror and back “SSO” outside models. Mirror comes assembled (Minor assembly required for the mounting bracket). Water-tight seal holding the mirror lens to the back-plate. | (SA-SSO34 Pictured) | Construction sites Parking Garages Roads & Streets Driveways to help you see traffic when an obstruction is blocking your view. Clearly see areas around a corner, hidden entrance way, or blind area. Recommended mounting height: 8 to 10 feet. |
| --- | --- | --- |

Round Convex Mirrors

| Description : Circular convex Stainless Steel mirror. Constructed of T-304 20 Gage stainless steel. Polished mirror to a NO:9 mirror finish. Both Stainless Steel Back (SA-SSOxx) and Hardboard Back (SA-SSxx) versions are glued and sealed to the mirror lens with a nylon molded rim around the mirror edge. Ball & Swivel Mounts with extension arms for flexible mounding needs. Shatterproof and unbreakable lens with excellent mirror qualities. Fully weatherproof SA-SSOxx version made to last for many years. The Stainless Steel Convex Mirrors have less of a convex curvature to the lens, which narrows the field of view and provides better visibility of distant objects. (Reflected objects around 100 feet away from the mirror appear approximately 25% larger when compared to the standard 160convex mirrors.) | INSIDE USE SA-SS14 SA-SS20 SA-SS26 SA-SS34 SA-SS42 OUTSIDE USE SA-SSO14 SA-SSO20 SA-SSO26 SA-SSO34 SA-SSO42 | Diameter 14” 20” 26” 34” 42” 14” 20” 26” 34” 42” |
| --- | --- | --- |
| View of the back-side of the SA-SSO34 (34”) Steel Backed outside use version. NOTE: The SA-SSO26, 34 and 42 inch mirrors, have double mounts as seen in this picture. The 14” and 20” mirrors have a single mount centered on the back. All mounting hardware seen in this picture is provided with the mirror. Anchor bolts or wall fasteners are NOT provided. |  |

# Text boxes

REFLECTION PRODUCTS

SAFETY AND SECURITY PRODUCTS

# Round Convex Steel Mirrors